## Slide 1
MAKERSUN.NET
PRESENTS
NUVOLA32
ESP32-S3 Breakout Board
DREAM. CODE. CREATE.
ESP32-S3
N16R8
Wi-Fi + BT
Blue Case
Manufactured by PCBWay

## Slide 2
OVERVIEW
NUVOLA32 — ESP32-S3 Breakout Board
What is NUVOLA32?
NUVOLA32 is a powerful development board based on the ESP32-S3, designed for makers, hobbyists, and professional developers who want to rapidly prototype IoT devices, audio systems, gaming consoles, and display interfaces — all on a single compact board.
2.4” DISPLAY
ILI9341 TFT Display on SPI1 Interface
SD Card
SPI0 Interface
LED
6 x CharliePlexing on GPIO 3 9 10
3W AUDIO
PCM5102 I2S DAC + Class-D Audio Amplifier + Speaker + Side Volume Pot
USB-C
CH340C for Arduino IDE / IDF
Auto-reset circuit for easy upload
LiPo Battery
USB/Battery automatic power selection + Charge LED Indicator

## Slide 3
FEATURES
GPIO Expansion Slot
1 - VCC
2 - GND
3 - MISO
4 - CLK
5 - MOSI
6 - GND
7 - SCL
8 - SDA
9 - GPIO8
10 - GPIO2
11 - GPIO1
12 - GND
SPI0 Shared with SD
RESET
LiPo Charging State LED
Power Switch
IO0 Button
Power LED
SD Card Slot
Volume Pot
Speaker

## Slide 4
FEATURES
Wi-Fi & Bluetooth 5
ESP32S3-WROOM-1 N16R8
Built-in dual-band connectivity
USB-C & Auto-Reset
CH340C for Arduino IDE / IDF
Auto-reset circuit for easy upload
Battery Management
MCP73831 battery charger
Battery monitor on GPIO6
8 I2C Buttons
PCF8574 via I2C
RST + BOOT included
3W Audio Output
PCM5102 I2S audio
Built-in 3W speaker output
Side volume potentiometer
2.4" TFT Display
ILI9341 320×240 px
Dedicated SPI1
SD Card Slot
SPI0 interface
Expandable storage
GPIO Expansion Slot
12-pin header: VCC, GND,
SPI0 shared, I2C, GPIO

## Slide 5
USE CASES
Perfect for every project
01
IoT & Smart Home
Sensors, home automation, cloud dashboards. Built-in Wi-Fi ready for MQTT, HTTP, WebSocket.
02
Portable Console
TFT display + 8 buttons + 3W audio = complete retro gaming platform out-of-the-box.
03
Audio Station
Audiophile-grade PCM5102 I2S DAC. Wi-Fi streaming, SD Card player, DSP equalizer. Side volume knob for direct control.
04
Rapid Prototyping
RST/BOOT, auto-reset, USB-C: zero config. From idea to firmware in minutes with Arduino IDE or IDF.

## Slide 6
TECHNICAL SPECIFICATIONS
Module
ESP32S3-WROOM-1 N16R8
Flash
16 MB
PSRAM
8 MB
Wireless
Wi-Fi 802.11 b/g/n + Bluetooth 5 / BLE
USB
Type-C (CH340C), Arduino IDE & ESP-IDF
Power
USB-C 5V or LiPoly Battery
Battery Charger
MCP73831, charging via USB-C
Battery Monitor
GPIO6
Buttons
8x tactile via PCF8574 (I2C) + RESET + BOOT
LEDs
6x Charlieplexing
Display
ILI9341 2.4" TFT 320×240 px (SPI1)
Audio
PCM5102 I2S DAC + 3W Amplifier + Side Volume Pot
Storage
MicroSD Card Slot (SPI0)
Switch
Physical ON/OFF
Case
Custom blue protective enclosure
Manufacturer
PCBWay

## Slide 7
NUVOLA32
The future of your maker projects is here.
Who is it for?
Makers & Hobbyists
Students & University researchers
Professional IoT developers
Retrogaming enthusiasts
Rapid prototypers
Where to buy?
🌐 Official Website
makersun.net
🏭 Manufacturer
PCBWay
📦 Open Source
Files & schematics available
DREAM. CODE. CREATE.